## Slide 1
Results
Summary and Future Plan
Background and Goals
Polydimethylsiloxane (PDMS) based solid phase microextraction (SPME) fibers are commonly used as a sampling tool for various volatile/semi-volatile compounds including gasoline residues via headspace (HS) concentration.
However, the compositions of volatile compounds in headspace (HS) via SPME sampling method usually differ from true compositions mainly because the partition coefficients of these compounds between headspace and a SPME fiber are not equal (Kfh).
The estimation of relative compositions of three vaporized hydrocarbons in headspace (HS) using ratios of partition coefficients (Kfh) obtained from inverse gas chromatography (IGC) and compare the results to those obtained from direct vapor analysis.
ACKNOWLEDGEMENTS
Office of Undergraduate Research
Chemistry Department
Theory of IGC
Probes: n-heptane, toluene, TMB
Carrier Gas: Hydrogen
Flow Rate: 10 mL/min at 25 C
Injection Volume: 0.01 mL
Inlet Temperature: 280 C
Oven Temperature: 90 and 130 C
Detector: Flame ionization detector (FID)
Inverse gas chromatography (IGC): measurement of interactions between gaseous solute (mobile phase) and solid (stationary phase), to produce retention volume (VN) at a given temperature (T) and a mass of solid phase (m).
Partition coefficient (K):
Relative partition coefficient (K/K”): relative compositions between analytes in headspace.
References
Kim, J.; Schmitz, M.; Al-Saigh, Z. Y., Application of Inverse Gas Chromatography for Quantitative Chemical Analysis of Volatile Compounds via Headspace-Solid Phase Microextraction, Forensic Chem. 2018, 11, 7-14.
HS analysis at 130 C
Experimental
PDMS (MW ~95,000)
PDMS solution in THF
n-heptane (x)
1,2,4-trimethylbenzene (z)
toluene (y)
Estimated headspace chemical compositions (from SPME sampling and partition coefficients) are comparable to true compositions via a direct headspace vapor injection method.
Partition coefficients via IGC measurements using capillary columns (DB1 phase) will be estimated.
Headspace containing more and various volatile compounds will be tested.
How to Estimate True Compositions of Volatile Compounds in Headspace Determined by Solid Phase Microextraction (HS/SPME)
Jamie Kim
Department of Chemistry, Buffalo State, SUNY
C0: concentration of analyte in a HS
Vf: volume of SPME fiber
Vh : volume of HS
t: retention time of a probe
tm: retention time of a marker
F: flowrate
J: correction factor
column packed with a material of interest
Vs: volume of stationary phase
m: mass of stationary phase : density of stationary phase
T: column temperature
: specific retention volume
Experimental Strategies
Coating on Chromosorb P
Sample | Compounds | PDMS SPME sampling composition | Estimated headspace composition (HScalc.) | Experimental headspace composition (HSexp.) | Relative % error
 | n-heptane | 10.5 (7) | 27.2 (16) | 28.7 (4) | -5.3
1 | toluene | 20.1 (7) | 35.4 (12) | 34.7 (1) | 2.0
 | TMB | 69.4 (14) | 37.4 (7) | 36.6 (5) | 2.2
 | n-heptane | 23.3 (8) | 43.6 (16) | 46.1 (3) | -5.4
2 | toluene | 29.9 (1) | 38.1 (3) | 37.0 (1) | 2.9
 | TMB | 46.8 (10) | 18.3 (4) | 16.9 (2) | 8.2
 | n-heptane | 3.7 (2) | 12.2 (7) | 13.2 (3) | -7.9
3 | toluene | 14.8 (5) | 32.7 (10) | 31.9 (5) | 2.7
 | TMB | 81.5 (7) | 55.1 (4) | 54.9 (7) | 0.3
PDMS coating on Chromosorb P and column preparation
 | Temperature (C) | 
 | 100 | 130
Kfh(toluene)/Kfh(n-heptane) | 1.54 (1) | 1.47 (1)
Kfh(TMB)/Kfh(n-heptane) | 6.72 (9) | 4.81 (3)
Relative partition coefficient at 100 and 130 C via IGC Measurements
HS analysis at 100 C
SPME fiber
HS-SPME sampling
Packing in the copper column
Headspace vial
(10 mL)
IGC measurements
Sample | Compounds | PDMS SPME sampling composition | Estimated headspace composition (HScalc.) | Experimental headspace composition (HSexp.) | Relative % error
 | n-heptane | 8.5 (1) | 27.7 (4) | 29.4 (5) | -5.4
1 | toluene | 17.1 (2) | 36.2 (8) | 35.0 (4) | 3.4
 | TMB | 74.4 (2) | 36.1 (1) | 35.7 (9) | 1.1
 | n-heptane | 18.9 (2) | 43.3 (8) | 46.3 (4) | -6.6
2 | toluene | 25.4 (4) | 37.8 (9) | 37.3 (1) | 1.3
 | TMB | 55.7 (6) | 19.0 (2) | 16.4 (3) | 15.5
 | n-heptane | 3.2 (1) | 13.2 (6) | 13.5 (3) | -1.9
3 | toluene | 12.9 (3) | 34.9 (10) | 32.2 (5) | 7.9
 | TMB | 83.9 (4) | 51.9 (3) | 54.2 (9) | -4.3
Preparation of headspace with different compositions for PDMS SPME and direct vapor analysis
probe molecule
injection
Adsorption-desorption
elution
gas
stationary phase
CH4
- tm
m